## Slide 1: Particle motion and sound propagation near boundaries
Mark W. Sprague, Phillip DeVille, and Joseph J. Luczkovich
East Carolina University
Greenville, NC, USA

## Slide 2: Fish in very shallow water (depth ≤ 10 m)
Boundaries affect sound propagation
Pressure/particle velocity relationship complicated near boundaries
Sound from deeper channels propagates into very shallow fish nesting areas
What is the particle velocity?
Do fish even detect the sound?

## Slide 3: Spatial change in velocity → Temporal change in pressure
Density
Sound speed
Spatial change
in velocity
Temporal change
in pressure

## Slide 4: Spatial change in pressure → temporal change in velocity
Density
Spatial change
in pressure
Temporal change
in velocity
Low p
High p
Low p
Low p
High p

## Slide 5: Hard Boundary
Simulation: Downward propagating plane wave of constant frequency
At boundary
Zero normal velocity
  Fish do not detect sound
Maximum pressure
  Hydrophone detects sound
Throughout water column:
Standing wave
Pressure and velocity nodes at different locations

## Slide 6: Pressure-release Boundary (Surface)
Simulation: Plane wave of constant frequency
At boundary
Zero pressure fluctuation
  Hydrophones do not detect sound
Maximum of normal velocity
  Fish detect sound
Throughout water column
Standing wave
Pressure and velocity nodes at different locations

## Slide 7: Soft Boundary (sand)
Simulation: Downward propagating plane wave of constant frequency
At boundary
Pressure and normal velocity continuous
Normal velocity nonzero
  Hydrophones and fish detect sound (different levels)
Throughout water column
Propagating wave

## Slide 8: Hard Boundary, propagation at angle
Simulation: Wave of constant frequency, 30° to normal
At boundary:
Zero normal velocity (vz)
Maximum parallel velocity (vx)
  Fish detect sound
Maximum pressure
  Hydrophones detect sound
Perfect reflection

## Slide 9: Soft Boundary (sand), propagation at angle
Simulation: Wave of constant frequency, 30° to normal
At boundary:
Parallel velocity (vx) discontinuous
Pressure and normal velocity (vz) continuous
Fish and hydrophones detect sound
Partial reflection, partial transmission

## Slide 10: Modelling Propagation with the FDTD
Finite difference time domain
  Pressure differences ➞ Particle velocity changes
  Particle velocity differences ➞ Pressure changes
Propagation from 10 m deep channel ➞ Shallow area (1 m or 2 m)
Sandy bottom
Source: 1 m deep in channel
10 m
1 m
1 m or 2 m

## Slide 11: Propagation – 2m deep, 100 Hz

## Slide 12: Propagation – 2m deep, 400 Hz

## Slide 13: Propagation – 1m deep, 100 Hz

## Slide 14: Propagation – 1m deep, 400 Hz

## Slide 15: Conclusions
Propagating sound waves have pressure and particle velocity fluctuations
Deep channel ➞ Shallow water propagation at bottom
Hydrophone measurements reported at AN2016 are relevant
  Significant sound exposure near vessel channels
Sound propagation modelling is useful for understanding pressure and particle velocity

## Slide 16
100 Hz, 1.75 m Depth
100 Hz, 30 m Range

## Slide 17
400 Hz, 30 m Range
400 Hz, 1.75 m Depth

## Slide 18
100 Hz, 0.75 m Depth
100 Hz, 30 m Range

## Slide 19
400 Hz, 30 m Range
400 Hz, 0.75 m Depth