## Slide 1: A new approach to regional hurricane evacuation and sheltering
NCEM, NWS and ECU Hurricane Workshop
May 18, 2011
Professor Rachel Davidson (University of Delaware)

## Slide 2: PROJECT TEAM
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 3: MOTIVATION
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Too many people
+
Too little road capacity
Traditional, conservative approach not feasible in some regions
Too soon
Unnecessary, expensive,
dangerous
Too late
Dangerous

## Slide 4: A NEW APPROACH
Broader decision frame 
New objectives (e.g., safety, cost)
New alternatives (shelter-in-place, phased evacuation) Direct integration & comparison of alternatives
Consider uncertainty in hurricane scenarios explicitly
Consider evacuation and sheltering together
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 5: OVERVIEW OF MODELS
Behavioral assumptions
North Carolina case study
Shelter model
Which shelters should be maintained over long-term?
Which should be opened in specific hurricane?
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Evacuation model
For approaching hurricane:
Who should stay home?
Who should evacuate and when?
Hurricane scenarios
Dynamic traffic modeling

## Slide 6: HAZARD MODELING
For shelter model
Long-term
Goal
Set of scenarios with adjusted occurrence probabilities
Represent all that could happen over long term
Are few in number
For evacuation model
Short-term
A
B
C
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Goal
Set of scenarios with adjusted occurrence probabilities
Represent all that could happen that are consistent with track to date
Are few in number

## Slide 7: LONG-TERM HAZARD MODELING
Develop large candidate set of hurricanes
For each, calc. wind speeds & coarse grid coastline surge levels
Find reduced set to minimize sum of errors wi,r and si,r
Calculate all find grid surge levels for reduced set
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Match hazard curves for each census tract
All historical or
synthetic events
NOAA Coastal Services Center
Reduced set of events with adjusted annual frequencies

## Slide 8: LONG-TERM HAZARD MODELING: RESULTS
Optimization-based Probabilistic Scenario (OPS) method
Huge computational savings
Can explicitly tradeoff num. hurricanes and error
Retains spatial coherence of individual hurricanes
Spatial correlation is largely captured
Can prioritize specific tracts, return periods
Only do computationally-intensive surge estimates for reduced set of events
Hazard curve errors for worst census tract
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 9: SHORT-TERM HAZARD MODELING
Estimated 135 possible scenarios based on Isabel (2003) with modifications
Central pressure deficit change (mb)
value=[-20 -10 0 10 20]
prob.=[.1 .2 .4 .2 1]
Along-track speed change (%) value=[-10 0 10]
prob.=[.25 .5 .25]
Heading change (degrees)
value=[-20 -15 -10 -5 0 5 10 15 20]
prob.=[.025 .075 .1 .15 .30 .15 .1 .075 .025]
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Sept. 16
17
18
19
20
Same for 1 day
Landfall
Scenario duration (3 days)

## Slide 10: HURRICANE SCENARIO-BASED ANALYSIS: KEY FEATURES
Each scenario is explicit
Capture probability distributions of wind/water/travel times
   Find strategies that are robust given uncertainty in hurricane tracks, intensities, speeds
Model wind and surge together
Can use state-of-the-art surge modeling
Could capture hurricane-specific features (e.g., track leading to earlier evacuation vs. directly onshore)
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 11: SHELTER PLANNING: MOTIVATION & OBJECTIVES
Objectives
Determine which shelters to maintain over the long-term
For each particular hurricane scenario, determine which shelters to open and how to allocate people to these shelters
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Motivation
Deliberate, focused planning for selected shelters
  Upgrade, prepare, plan for them
Shelter locations affect traffic
   Locate them to alleviate traffic

## Slide 12: SHELTER MODEL STRUCTURE
Inputs
Evacuation demand; hurricane scenarios and probabilities; destinations
Lower-level
For each scenario:
What route does each driver take given shelter locations?
What are expected travel times?
Lower-level:
Traffic Assignment Model
Outputs
Shelter plan and performance by scenario (shelter use, travel times)
Upper-level:
Shelter Location-Allocation
Upper-level
Which shelters to maintain over the long-term?
For a certain hurricane scenario, which shelters to open and how to allocate people to these shelters by origin?
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Shelter plan
Travel times

## Slide 13: SHELTER UPPER-LEVEL MODEL
OBJECTIVE
CONSTRAINTS
Minimize weighted sum of expected (over all hurricane scenarios):
  Total evacuee travel time
  Unmet shelter demand
Shelters
  Can not maintain more than max. allowable number of shelters
  In each scenario, can only open shelter if one is located there and is safe for that scenario
  In each scenario, num. evacuees going to a shelter cannot exceed shelter capacity
Staffing
  For each scenario, cannot exceed available number of staff
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 14: SHELTER LOWER-LEVEL MODEL
OBJECTIVE
Minimize
  Each driver’s own perceived travel time
  (stochastic user equilibrium)
  For each scenario, given open shelters as determined in upper-level
  Describes individual drivers’ route choice behavior
  Independent decision makers
  Only passenger cars
  2 types of evacuees, headed to:
    Public shelter
    Destination other than a public shelter
      Assumption 1: Leave threatened area quickly as possible
      Assumption 2: Fixed destinations
  Peak flow analysis for traffic
Assumptions
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 15: SHELTER MODEL SOLUTION
Upper-level
Find candidate shelter locations and O-D matrices by solving upper-level with travel times fixed
Test for optimality?
End
No
Initialization:
Free-flow travel times
Yes
Lower-level
For each scenario, solve SUE problem to find flow pattern, link travel times, and average travel times for each O-D
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 16: SHELTER MODEL CASE STUDY INPUTS
Highway network
7691 bi-directional links
5055 nodes at origins,
destinations, link intersections
Origins and destinations
Origins: 529 eastern census tracts
Destinations: 187 potential shelter locations from ARC (capacity 700-4000)
  Exits from evacuation area (vary by scenario; about 3 to 5)
Evacuation and shelter demand
Estimated using HAZUS-MH
Hurricane scenarios
33 hurricane scenarios with annual occurrence probabilities estimated using OPS method based on wind speeds
Shelters
3000 staff available
Can maintain at most 50 shelters
Free flow speed=55 mph
Capacity per lane: 1500 vph
2 people/vehicle
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 17: SHELTER MODEL CASE STUDY INPUTS
Highway network
Possible shelters
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 18: SHELTER MODEL CASE STUDY RESULTS
Recommendation of shelters to maintain
Initial solution
(not considering effect shelter location has on travel times)
107
59
30
50
103
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 19: SHELTER MODEL CASE STUDY RESULTS
Optimized solution
(considering effect shelter location has on travel times)
48
131
39
14
13
Recommendation of shelters to maintain
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
50 shelters selected
Most to the west of I-95, I-40
Considering traffic suggests moving some shelters.

## Slide 20: SHELTER MODEL CASE STUDY RESULTS
20
Illustrative hurricane scenario
Evacuation demand: 410,000
Shelter demand: 44,260
Peak wind: 175 mph (Category 5)
Landfall near Wilmington, then travels north along coast
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 21: SHELTER MODEL CASE STUDY RESULTS
Illustrative hurricane scenario
(Assuming nonshelter evacuees exit quickly as possible)
Shelter use and total traffic flows
I-40
US-74
US-70
NC-24
To Raleigh-Durham
To Charlotte and S. Carolina
To Greensboro
Wilmington
Jacksonville
Morehead
Northbound I-40 and Rte 74 heavy
Some shelters in west not needed
Some shelters in east cannot be used
Congestion b/c many to Raleigh/Durham
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Thickest line = 7500 vph

## Slide 22: SHELTER MODEL CASE STUDY RESULTS
NC-24
Illustrative hurricane scenario
(Assuming nonshelter evacuees exit quickly as possible)
Shelter use and traffic flows to shelters only
NC-24 heavily used
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Initial solution
(not considering effect shelter location has on travel times)
Thickest line = 750 vph

## Slide 23: SHELTER MODEL CASE STUDY RESULTS
23
Illustrative hurricane scenario
(Assuming nonshelter evacuees exit quickly as possible)
Shelter use and traffic flows to shelters only
Little traffic on congested roads
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Thickest line = 750 vph
Optimized solution
(considering effect shelter location has on travel times)

## Slide 24: SHELTER MODEL CASE STUDY RESULTS
Different assumption for non-shelter evacuees
Two types of evacuees: To shelter or not
For evacuees not going to a public shelter
  Leave evacuation area as quickly as possible
  Fixed destinations
  (Outer Banks to VA; others evenly distributed between 5 cities)
Virginia
Greensboro
Raleigh
Charlotte
Fayetteville
Durham
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 25: SHELTER MODEL CASE STUDY RESULTS
Scenario | Number evacuating | Number who use shelters | Average travel time to a shelter |  |  |  |  | 
 |  |  | Leave area quickly as poss. |  |  | Fixed destinations |  | 
 |  |  | Initial iteration | Optimal iteration | % reduction | Initial iteration | Optimal iteration | % reduction
1 | 566,530 | 62,550 | 4.11 | 3.41 | 21% | 10.2 | 3.16 | 222%
2 | 411,860 | 44,260 | 2.85 | 2.49 | 14% | 3.28 | 2.46 | 33%
3 | 323,110 | 35,537 | 2.69 | 2.57 | 5% | 3.33 | 2.7 | 24%
4 | 325,360 | 34,154 | 2.18 | 2.06 | 6% | 4.9 | 2.3 | 113%
… | … | … | … | … | … | … | … | …
Reduction in travel time for shelterees depends on scenario
Reduced 6.7% on average across all trips; 20+% for many scenarios
Benefit more pronounced with fixed destinations
Choosing shelter locations carefully can reduce travel times
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 26: SHELTER MODEL CASE STUDY RESULTS
Fixed destination assumption for non-shelter evacuees
Scenario #1
Shelter use and traffic flows to shelters only
Initial solution
Optimized solution
Raleigh
Durham
Charlotte
In initial solution many housed in Charlotte  traffic
In optimal solution, evacuees shifted to Raleigh/Durham  alleviates traffic
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 27: SHELTER PLANNING: CONCLUSIONS
Choice of shelters to maintain over long-term
  Carefully choose subset
  Easier to upgrade, prepare, plan for smaller set
  Can select so that they are robust in range of hurricane scenarios
Choice of shelters to open in specific hurricane
  Can choose so as to alleviate traffic
  Direct shelter evacuees away from non-shelter evacuees’ routes
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions

## Slide 28: EVACUATION PLANNING: MOTIVATION & OBJECTIVES
Motivation
Want a strategy that is good on average and robust across all possible scenarios
Consider phased evacuation and sheltering-in-place
Objectives
For approaching hurricane:
Who should stay home?
Who should evacuate and when?
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Minimize risk
Minimize travel times/cost
Normative

## Slide 29: EVACUATION MODEL STRUCTURE
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Inputs
Population at origins; hurricane scenarios and probabilities; shelter capacity; risk
Lower-level
(disaggregated areas & time steps)
For each scenario:
What route does each driver take given evacuation plan?
What are expected travel times?
What is the expected risk?
Lower-level:
Traffic Assignment Model
Outputs
Evacuation plan and performance by scenario (risk, travel times)
Upper-level:
Evacuation Model
Upper-level
(aggregated areas & time steps)
Who should stay home?
Who should go to shelters and when?
Who should go non-shelters and when?
Evac.
plan
Travel times

## Slide 30: EVACUATION UPPER-LEVEL MODEL
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
OBJECTIVE
CONSTRAINTS
Minimize weighted sum of expected (over all hurricane scenarios):
  Risk at home
  Risk while traveling
  Risk at destination
  Risk beyond threshold (k2)
Shelters
  In each scenario, num. evacuees going to a shelter cannot exceed shelter capacity
Conservation of people
  People must stay, go to a shelter, or go to a non-shelter
Definitions
  Define critical risk as num. people in danger above a threshold
  Define risk at home, while traveling, at destination
  Define total travel times
  Total travel time to shelters (k1)
  Total travel time to non-shelters (k1)
  Penalty for leaving early (k3)

## Slide 31: EVACUATION UPPER-LEVEL MODEL
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Definition of risk
Probability of being in danger (killed, injured, having a traumatic experience)
Would rather evacuate than experience this
Destination
Home
Destination
Home
Risk for each person in hurricane h in location l
= max{P(being in danger from surge or wind at any t in location l)}

## Slide 32: EVACUATION LOWER-LEVEL MODEL
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
OBJECTIVE
Minimize
  Total travel time over network and planning horizon
  (dynamic traffic assignment)
  Dynamic traffic assignment (vs. equilibrium) necessary to know who is where and when.
  Intersection of people and flood/wind in space and time creates risk.
  Very fast model to run!
Key features

## Slide 33: EVACUATION MODEL CASE STUDY INPUTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Highway network
7691 bi-directional links
5055 nodes at origins,
destinations, link intersections
Origins and destinations
Origins: 66 zip-code-based evacuation zones
Destinations: 100 potential shelter locations (≈ those used in Isabel) 6 exits from evacuation area
Population: Only residents from census
Hurricane scenarios
Only actual Isabel track
7 hurricane scenarios w/estimated occurrence probabilities
Risk functions: As shown
User-specified parameters: t=6 hours; T=72 hours
k1 (travel)=0.001; k2 (critical risk)=0; k3 (early penalty)= 0.0004;
Free flow speed=55 mph
Capacity per lane: 1500 vph
2 people/vehicle
2 runs

## Slide 34: EVACUATION MODEL CASE STUDY INPUTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
7 scenarios | Occurrence probability
Isabel | 0.54
Divert north | 0.18
Divert south | 0.18
Divert far north | 0.04
Divert far south | 0.04
Best case northernmost highest cen. pressure deficit slowest forward speed | 0.01
Worst case southernmost lowest cen. pressure deficit fastest forward speed | 0.01
Isabel

## Slide 35: EVACUATION MODEL CASE STUDY RESULTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Evacuation plan. Plan based on actual Isabel track only.
(ktravel=0.001, kcritical_risk=0, kearlypenalty=0.0004)
Total number of people | Plan based on Isabel only
Leaving to shelters | 32,700
Leaving not to shelters | 141,200
Staying home | 2,977,500
Chart: Number of people evacuating
| 18:00 | 0:00 | 6:00 | 12:00 | 18:00 | 0:00 | 6:00 | 12:00 | 18:00 | 0:00 | 16-Sep | 17-Sep | 18-Sep | 19-Sep
 | 22935 | 24904 | 25333 | 26150 | 26547 | 27257 | 16531 | 4228 | 0 | 0
Landfall

## Slide 36: EVACUATION MODEL CASE STUDY RESULTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Evacuation plan. Plan based on actual Isabel track only.
(ktravel=0.001, kcritical_risk=0, kearlypenalty=0.0004)
% of population that stays home
Num. leaving hours before landfall
48
42
36
30
24
18
12
6
0
Some start later or end earlier. Spread out evacuation as possible.

## Slide 37: EVACUATION MODEL CASE STUDY RESULTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Performance. Plan based on actual Isabel track only.
(ktravel=0.001, kcritical_risk=0, kearlypenalty=0.0004)
 | Scenario that actually occurs | Occ. Prob. | All risk | Home risk | Travel risk | Shelter risk
1 | Isabel | 0.54 | 7,202 | 7,180 | - | 22
2 | Divert north | 0.18 | 167 | 160 | 4 | 3
3 | Divert south | 0.18 | 183,174 | 182,880 | 81 | 213
4 | Divert far north | 0.04 | 6 | - | 6 | -
5 | Divert far south | 0.04 | 335,195 | 334,750 | 318 | 127
6 | Best | 0.01 | 604 | - | 604 | -
7 | Worst | 0.01 | 336,903 | 335,580 | 1,065 | 258
 | Expected value |  | 53,806 | 53,709 | 39 | 58
 | Total travel time (million person-minutes)
To shelters | 2.2
To non-shelters | 18.7

## Slide 38: EVACUATION MODEL CASE STUDY RESULTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Evacuation plan comparison.
(ktravel=0.001, kcritical_risk=0, kearlypenalty=0.0004)
Chart: Num. people evacuating
| 18:00 | 0:00 | 6:00 | 12:00 | 18:00 | 0:00 | 6:00 | 12:00 | 18:00 | 0:00 | 16-Sep | 17-Sep | 18-Sep | 19-Sep
7 hurricane | 38729 | 40535 | 94759 | 95516 | 95958 | 31820 | 59900 | 9876 | 0 | 0
Isabel only | 22935 | 24904 | 25333 | 26150 | 26547 | 27257 | 16531 | 4228 | 0 | 0
Total number of people | Plan based on | 
 | Isabel only | 7 hurricanes
Leaving to shelters | 32,700 | 33,000
Leaving not to shelters | 141,200 | 434,100
Staying home | 2,977,500 | 2,684,700
Landfall

## Slide 39: EVACUATION MODEL CASE STUDY RESULTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Evacuation plan comparison.
(ktravel=0.001, kcritical_risk=0, kearlypenalty=0.0004)
Total number of people | Plan based on | 
 | Isabel only | 7 hurricanes
Leaving to shelters | 32,700 | 33,000
Leaving not to shelters | 141,200 | 434,100
Staying home | 2,977,500 | 2,684,700

## Slide 40: EVACUATION MODEL CASE STUDY RESULTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Evacuation plan comparison.
(ktravel=0.001, kcritical_risk=0, kearlypenalty=0.0004)
Isabel only plan
% of population that stays home
7 hurricane plan
% of population that stays home

## Slide 41: EVACUATION MODEL CASE STUDY RESULTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Isabel only plan
7 hurricane plan
Num. leaving hours before landfall
48
42
36
30
24
18
12
6
0
Num. leaving hours before landfall
48
42
36
30
24
18
12
6
0
Evacuation plan comparison.
(ktravel=0.001, kcritical_risk=0, kearlypenalty=0.0004)

## Slide 42: EVACUATION MODEL CASE STUDY RESULTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Performance comparison.
(ktravel=0.001, kcritical_risk=0, kearlypenalty=0.0004)
 | Scenario that actually occurs | Home risk |  | Travel risk |  | Shelter risk | 
 |  | Isabel | 7 hurr. | Isabel | 7 hurr. | Isabel | 7 hurr.
1 | Isabel | 7,180 | 146 | - | - | 22 | -
2 | Divert north | 160 | 27 | 4 | 2 | 3 | -
3 | Divert south | 182,880 | 8,713 | 81 | 13 | 213 | 39
4 | Far north | - | - | 6 | 3 | - | -
5 | Far south | 334,750 | 43,810 | 318 | 420 | 127 | -
6 | Best | - | - | 604 | 882 | - | -
7 | Worst | 335,580 | 43,810 | 1,065 | 3,155 | 258 | 15
 | Expected value | 53,709 | 3,865 | 39 | 44 | 58 | 7

## Slide 43: EVACUATION MODEL CASE STUDY RESULTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Performance comparison.
(ktravel=0.001, kcritical_risk=0, kearlypenalty=0.0004)
 | Total travel time (million person-minutes) | 
 | Isabel only plan | 7 hurricane plan
To shelters | 2.2 | 2.2
To non-shelters | 18.7 | 57.4
In 7-hurricane plan, more people evacuated due to uncertainty in scenario
lower risk for all scenarios (although still some risk)
higher travel times

## Slide 44: EVACUATION MODEL CASE STUDY RESULTS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Tradeoff between minimizing risk and minimizing travel time
Performance. Plan based on actual Isabel track only.
(ktravel=varying, kcritical_risk=0, kearlypenalty=0.0004)
Chart: k1 (weight on travel time)
| 1E-3 | 3.0000000000000001E-3 | 6.0000000000000001E-3 | 8.9999999999999993E-3
Risk | 7202 | 7203 | 9832 | 38922
Total travel time | 20908000 | 20862000 | 20382000 | 16612000

## Slide 45: CONCLUSIONS
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Broader decision frame 
New objectives (e.g., safety, cost)
New alternatives (shelter-in-place, phased evacuation) Direct integration & comparison of alternatives
Consider uncertainty in hurricane scenarios
Considering evacuation and sheltering together

## Slide 46: ON-GOING/POSSIBLE FUTURE WORK
Introduction
Hazard models
Shelter model
Evacuation model
Conclusions
Hazard modeling
Develop more systematic approach to real-time generation of short-term scenarios
Shelter modeling
Run with dynamic traffic assignment model, better input
Address people with various functional and developmental impairments
Incorporate results from behavioral survey
Consider shelter investments and budget constraint
Evacuation modeling
Examine results in more depth, incl. effect of varying ki weights
Address different groups of people (e.g., mobile homes, tourists)
Consider contraflow plan, road closures
Incorporate results from behavioral survey/Make more descriptive
Two-stage analysis
Your ideas?

## Slide 47: ACKNOWLEDGEMENTS
Partners
NC Division of Emergency Management
American Red Cross-North Carolina
Undergraduate students
Paige Mikstas
Sophia Elliot
Samantha Penta
Kristin Dukes
Andrea Fendt
Vincent Jacono
Michael Sherman
Madison Helmick
Gab Perrotti
Inna Tsys